## Slide 1: Fault Models for Non-electrical Disciplines in Verilog-AMS
Supervisor: Prof. Franco Fummi
Candidate: Alessandra Castiglioni
Advisors: Dr. Nicola Dall’Ora
Dr. Enrico Fraccaroli

## Slide 2: Outline
Introduction
State of the Art and Technologies
Taxonomy Definition
Framework Creation
Experimental Results
Conclusions

## Slide 3: Open Issues
Smart SoC systems need to interact with different physical domains
To do safety or production analysis it is necessary to inject faults
Only electrical faults are tested
Inject and simulate non-electrical faults
Standardize faults
Automatize fault simulation

## Slide 4: State of the Art
It is challenging to model faults suitable for any physical model representation
For the simulation of physical systems
  Graphical tools
  Description Languages
Verilog-AMS is used to simulate the models
  Injecting faults is immediate compared to graphical tools
“Functionality and fault modeling of a dc motor with verilog-ams” (2020)
“Multi-discipline fault modeling with verilog-ams“ (2020)

## Slide 5: How?
From the electrical models we build fault models on non-electrical domains
Verilog-AMS allows us to do this given a variety of physical disciplines
Name | Potential | Flow
Electrical | Voltage | Current
Magnetic | Magneto Motive Force | Flux
Thermal | Temperature | Power
Kinematic | Position | Force
Rotational | Angle | Angular Force
We can model faults on all domains in verliog-AMS

## Slide 6: Used technologies
Verilog – AMS
TCL
HIF Suite

## Slide 7: Fault Taxonomy
Domain | Open | Short | Parametric
Electrical | resistor | resistor | alter internal component value
Rotational | damper |  | 
Kinematic | damper |  | 
Faults modeled with the Verilog-AMS language

## Slide 8: Fault Taxonomy
Domain | Open equation | Short equation
Electrical | V(branch) <+ I(branch)*value | I(branch) <+ V(p,n)/small value
Rotational | Tau(shaft) <+ Omega(shaft)*(-value) | 
Kinematic | F(velocity) <+ Pos(z)*(-value) | 
Faults modeled with the Verilog-AMS language through the following equations:

## Slide 9: A Framework for Injecting and Simulating Faults
Fault-Free Verilog-AMS Model
HIF Suite
HIF tool
Faulty Verilog-AMS Model
Testbench
TCL script
Fault simulation

## Slide 10: Fault Injector Architecture
Top Testbench
Comparator
Initialization
Testbench T2
Testbench T1
Fault-free Model
Faulty Model
Init model
Init model
TCL script
1 simulation for each fault
outputs
fault selection
results.txt
ID of each fault detected
case statement

## Slide 11: HIF Tool
HIF tool
Discipline
types?
Fault-free Model
Switch case
for electrical discipline
Switch case for mechanical discipline
Switch case
for kinematics discipline
Faulty Model

## Slide 12: Experimental Validation
Motor model

## Slide 13: Experimental Validation
MEMS model

## Slide 14: Conclusions
Non-electrical faults were modeled and simulated on heterogeneous systems
A taxonomy has been created for non-electrical faults
A framework has been created to automate the processes of modeling, injection and simulation of faults
Future works
  Take into account other types of non-electrical faults to improve taxonomy
  Increase the degree of automation of the framework